## Slide 1
MODULE 1
Introduction to Design of Experiments
Why systematic experimentation beats trial-and-error DOE Helper Training Course
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 2
What You Will Learn
What Design of Experiments (DOE) is and why it matters
The cost of unplanned experiments
The One-Variable-At-a-Time (OVAT) trap
Core DOE concepts: factors, levels, responses, effects
How doe-helper automates the DOE workflow
When to use DOE vs. other approaches
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 3
What is Design of Experiments?
A systematic method for planning experiments
  Change multiple factors simultaneously
  Use statistical principles to extract maximum information
  Minimise the number of experimental runs needed
Pioneered by R.A. Fisher in the 1920s for agriculture
Extended by Taguchi, Box, and others for industry
Now applied to software, cloud, manufacturing, and beyond
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 4
The Cost of Unplanned Experiments
THE PROBLEM
Ad-hoc testing wastes resources
Interactions between factors are missed
Conclusions drawn from insufficient data
Optimisation gets stuck in local optima
Results are not reproducible
REAL-WORLD EXAMPLE
A web team ran 47 ad-hoc tests over 3 months
Found: only 2 factors mattered
A 2-factor full factorial needed just 4 runs
DOE saved 43 runs and 11 weeks
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 5
The OVAT Trap
One-Variable-At-a-Time: change one factor, hold others constant
Seems logical but has critical flaws:
  Misses interactions between factors entirely
  Requires more runs to learn the same amount
  Can converge on the wrong optimum
Example: tuning a web server
  OVAT: 3 factors × 3 levels = 9 runs, misses interactions
  Full factorial: 2³ = 8 runs, captures all interactions
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 6
Core DOE Concepts
Factor — a variable you control (e.g. temperature, cache size)
Level — specific value of a factor (e.g. low/high, 100/200/300)
Response — what you measure (e.g. throughput, yield, cost)
Main Effect — the average impact of one factor on the response
Interaction — when the effect of one factor depends on another
Design Matrix — the table of all planned experimental runs
Randomisation — running in random order to avoid bias
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 7
Effect Sparsity Principle
In most systems only a few factors have large effects
Most interactions are negligible
This is the "Pareto of experimentation"
Screening designs exploit this: test many factors cheaply
Then focus detailed experiments on the vital few
doe-helper supports this: screen → refine → optimise
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 8
The DOE Workflow
1. Define objectives — what do you want to learn or optimise?
2. Select factors and levels — what can you control?
3. Choose a design — how many runs can you afford?
4. Generate the design matrix and run experiments
5. Analyse results — which factors matter?
6. Interpret and act — confirm, refine, or optimise
doe-helper automates steps 3–6 and guides 1–2
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 9
Meet doe-helper
terminal
$ pip install doehelper
$ doe init reactor --design full_factorial
Created: reactor/config.json
$ doe generate reactor/
Design matrix written to reactor/design.csv
Runner script written to reactor/run.sh
$ doe analyze reactor/
ANOVA table, Pareto chart, main-effects plots
$ doe optimize reactor/
Recommended: temperature=180, pressure=3.5
doe-helper provides a complete CLI workflow from design to optimisation
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 10
Key Takeaways
DOE is a systematic, statistically rigorous way to experiment
OVAT wastes runs and misses interactions
Effect sparsity: most systems have only a few important factors
doe-helper automates the entire DOE workflow via the CLI
The workflow: define → design → run → analyse → optimise
© 2026 Martin J. Gallagher | GPL-3.0-or-later

## Slide 11
HANDS-ON EXERCISE
Exercise 1: Explore doe-helper
1. Install doe-helper: pip install doehelper
2. Run: doe --help and read the available commands
3. Run: doe init coffee_brewing --design full_factorial
4. Open coffee_brewing/config.json and examine the template
5. Identify the factors, levels, and responses
Bonus: Think of a problem in your own work where OVAT
has been used. How many factors and levels would a
proper DOE need?
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com