## Slide 1
MODULE 4
Fractional Factorial & Screening Designs
Testing many factors efficiently when resources are limited
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 2
Learning Objectives
Understand why fractional factorials exist
Learn about resolution and aliasing
Use Plackett-Burman and Definitive Screening designs
Choose the right screening design with doe-helper
Interpret confounded effects
Plan a follow-up experiment after screening
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 3
The Problem: Too Many Factors
Full factorial with 7 factors = 128 runs
With 10 factors = 1,024 runs
With 15 factors = 32,768 runs!
In practice, experiments often start with 6–20 factors
Effect sparsity says most factors won't matter
Solution: run a fraction of the full factorial
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 4
Fractional Factorial Designs
Run 2ᵏ⁻ᵖ instead of 2ᵏ runs
  2⁷⁻⁴ = 8 runs instead of 128 for 7 factors
  2⁶⁻² = 16 runs instead of 64 for 6 factors
Trade-off: some effects become aliased (confounded)
Resolution tells you what is confounded:
  Res III: main effects aliased with 2-factor interactions
  Res IV: main effects clear, 2FI aliased with each other
  Res V: main effects and 2FI all clear
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 5
Fractional Factorial with doe-helper
terminal
{
"factors": {
"A": {"low": -1, "high": 1},
"B": {"low": -1, "high": 1},
"C": {"low": -1, "high": 1},
"D": {"low": -1, "high": 1},
"E": {"low": -1, "high": 1},
"F": {"low": -1, "high": 1},
"G": {"low": -1, "high": 1}
},
"responses": {
"performance": {"units": "score", "target": "maximize"}
},
"design": {"type": "fractional_factorial"}
}
$ doe generate screening/
$ doe info screening/ # shows aliasing structure
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 6
Plackett-Burman vs. Definitive Screening
PLACKETT-BURMAN
Plackett-Burman (PB)
Run counts: multiples of 4 (12, 20, 24…)
Screen up to N−1 factors in N runs
Resolution III
Main effects aliased with 2FIs
No curvature detection
Best for: initial rough screening
DEFINITIVE SCREENING
Definitive Screening (DSD)
2k+1 runs for k factors
Three-level design (low/mid/high)
Main effects NOT aliased with 2FIs
Can detect curvature
Modern best practice (Jones 2011)
Best for: cleaner screening
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 7
The Screening Workflow
Phase 1: Screen
  Run PB or DSD with all candidate factors
  Identify 3–5 significant factors, drop the rest
Phase 2: Characterise
  Full factorial on surviving factors
  Estimate all interactions, check for curvature
Phase 3: Optimise
  Response surface design (CCD, Box-Behnken)
  doe optimize for final settings
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 8
Fold-Over with doe augment
terminal
# After screening, de-alias confounded effects:
$ doe augment api_screening/ --method fold-over
# Mirrors the original design to break aliases
# Doubles run count but separates confounded effects
# Other augmentation methods:
$ doe augment experiment/ --method center-points --count 5
$ doe augment experiment/ --method star-points
doe augment extends an existing design without starting over
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 9
Key Takeaways
Fractional factorials trade runs for information (aliasing)
Resolution tells you what's confounded with what
Plackett-Burman: maximum screening efficiency
Definitive Screening: modern, cleaner main-effect estimates
doe augment extends designs with fold-overs and star points
© 2026 Martin J. Gallagher | GPL-3.0-or-later

## Slide 10
HANDS-ON EXERCISE
Exercise 4: Screening a Microservice
Scenario: 8 factors that might affect API latency.
1. Create config.json with 8 continuous factors
2. Set design type to "plackett_burman"
3. Run: doe generate microservice/
  How many runs does the design require?
4. Compare: change to "definitive_screening"
  How many runs now? What's different?
5. Run the simulation and analyse results
6. Which factors appear significant?
7. Plan a follow-up design with the significant factors
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com