## Slide 1
MODULE 7
Multi-Response Optimisation & Advanced Topics
Balancing competing objectives and extending designs
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 2
Learning Objectives
Optimise for multiple responses simultaneously
Understand desirability functions
Use design augmentation strategies
Apply blocking and randomisation correctly
Use Taguchi designs for robust parameter design
Handle mixture experiments
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 3
Multi-Response Optimisation
Most real experiments have multiple responses
  Maximise yield AND minimise cost
  Minimise latency AND maximise throughput
Responses often conflict: improving one degrades another
Derringer-Suich desirability function:
  Transform each response to a 0–1 desirability scale
  Overall D = geometric mean of individual dᵢ
  D = 1: perfect | D = 0: unacceptable
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 4
Multi-Response Config & Optimization
terminal
{
"responses": {
"yield": {"units": "%", "target": "maximize"},
"cost": {"units": "USD", "target": "minimize"},
"purity": {"units": "%", "target": 99.5}
}
}
$ doe optimize reactor_multi/
Optimization Results:
yield=91.2%, cost=$42.30, purity=99.3%
Overall desirability: 0.87
doe optimize balances all responses via desirability functions
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 5
Design Augmentation
Often you want to extend an existing design
doe augment supports several strategies:
  Fold-over: mirror design to break aliases
  Star points: add axial points for RSM
  Center points: add runs at the center
Benefits:
  Leverages data you already have
  Sequentially builds up information
  No need to start over from scratch
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 6
Taguchi & Mixture Designs
ROBUST DESIGN
Taguchi Designs
Focus on robustness to noise
Inner array: controllable factors
Outer array: noise factors
S/N ratio as the response
doe-helper: "type": "taguchi"
MIXTURES
Mixture Experiments
Proportions must sum to 1
E.g. concrete, alloys, formulations
Simplex-Lattice: evenly spaced
Simplex-Centroid: vertices + center
doe-helper: "type": "simplex_lattice"
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 7
Blocking & D-Optimal Designs
Blocking accounts for known nuisance variables
  Different batches, days, operators, machines
  Block effects are estimated and removed from analysis
  doe-helper: set "blocks" in the design section
D-Optimal: computer-generated for non-standard situations
  Irregular factor space, constraints
  Mix of continuous and categorical factors
  doe-helper: "type": "d_optimal", "runs": N
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 8
Power Analysis with doe-helper
terminal
$ doe power experiment/
Power Analysis
Design: full_factorial (2^3)
Runs: 8
Error est.: 2.5 (from prior data or estimate)
Detectable Effect Sizes (80% power, alpha=0.05):
Main effects: 3.2 units
2-factor int.: 3.2 units
$ doe power experiment/ --effect-size 5.0
Power: 0.95 for main effects
Power: 0.95 for 2-factor interactions
Power analysis ensures your design can detect meaningful effects
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com

## Slide 9
Key Takeaways
Multi-response: desirability functions balance trade-offs
doe augment extends designs without starting over
Blocking removes nuisance variation systematically
Taguchi designs optimise for robustness to noise
D-Optimal handles constraints and irregular spaces
© 2026 Martin J. Gallagher | GPL-3.0-or-later

## Slide 10
HANDS-ON EXERCISE
Exercise 7: Multi-Response Optimisation
1. Add 3 responses to the reactor experiment:
  yield (maximize), cost (minimize), purity (target: 99.5)
2. Run: doe optimize reactor_multi/
  What is the overall desirability score?
  Which response is most compromised?
3. Run: doe power reactor_multi/
  Is the design adequately powered?
4. Try: doe augment reactor_multi/ --method center-points --count 4
  How does augmentation change the power analysis?
© 2026 Martin J. Gallagher | GPL-3.0-or-later | doehelper.com