## Slide 1
MODULE 3
Full Factorial Designs
Understanding and running complete two-level experiments
Copyright © 2026 Martin J. Gallagher. Licensed under GPL-3.0-or-later.

## Slide 2
Learning Objectives
Understand full factorial (2^k) designs
Calculate the number of runs needed
Interpret main effects and interactions
Generate and run a full factorial with doe-helper
Read ANOVA tables and Pareto charts
Know when full factorial is the right choice

## Slide 3
What is a Full Factorial Design?
Tests every combination of factor levels
For k factors at 2 levels: 2^k runs
  2 factors: 4 runs
  3 factors: 8 runs
  4 factors: 16 runs
  5 factors: 32 runs
Estimates ALL main effects and ALL interactions
The "gold standard" of experimental designs
Practical limit: ~5-6 factors (32-64 runs)

## Slide 4
2^2 Full Factorial Example
Design Matrix & Results
Factor A: Temperature (150, 200)
Factor B: Pressure (1, 5)
Run 1: A=low, B=low -> 62%
Run 2: A=high, B=low -> 74%
Run 3: A=low, B=high -> 68%
Run 4: A=high, B=high -> 91%
Effect Calculations
Main effect A = [(74+91)-(62+68)]/2
= 17.5% (Temperature matters)
Main effect B = [(68+91)-(62+74)]/2
= 11.5% (Pressure matters)
Interaction AB = [(62+91)-(74+68)]/2
= 5.5% (Synergy!)

## Slide 5
Why Interactions Matter
An interaction means the effect of one factor depends on another
OVAT cannot detect interactions at all
Example: Temperature alone increases yield by 17.5%
  But at high pressure, temperature boost is even larger
  The combination is more powerful than either alone
Interactions can be antagonistic too (cancel each other out)
Full factorials capture all of these relationships

## Slide 6
Running a Full Factorial with doe-helper
# 1. Configure
$ cat > seal_strength/config.json << 'EOF'
{
"factors": {
"temperature": {"low": 225, "high": 285, "units": "F"},
"pressure": {"low": 40, "high": 90, "units": "psi"},
"dwell_time": {"low": 1.0, "high": 3.5, "units": "sec"}
},
"responses": {
"seal_strength": {"units": "g/in", "target": "maximize"}
},
"design": {"type": "full_factorial", "center_points": 3}
}
EOF
# 2. Generate the design matrix
$ doe generate seal_strength/
# 3. Run experiments and record results
$ doe record seal_strength/
# 4. Analyse
$ doe analyze seal_strength/

## Slide 7
Reading the ANOVA Table
ANOVA = Analysis of Variance
Key columns:
  Source: factor or interaction name
  SS: Sum of Squares (variability explained)
  DF: Degrees of Freedom
  MS: Mean Square (SS / DF)
  F-value: test statistic (higher = stronger effect)
  p-value: probability effect is due to chance
Rule of thumb: p < 0.05 means the factor is significant

## Slide 8
Reading the Pareto Chart
Bar chart of absolute effect magnitudes, sorted largest to smallest
Dashed reference line shows significance threshold
Bars above the line are statistically significant effects
Quickly identifies the "vital few" factors
doe-helper generates this automatically with doe analyze

## Slide 9
Center Points
Extra runs at the midpoint of all factors
Purpose: detect curvature (non-linear effects)
If center-point average differs from predicted linear value:
  The true relationship is curved
  You may need a response surface design
Cheap insurance: 3-5 center points cost little
doe-helper: set center_points in config.json

## Slide 10
Key Takeaways
Full factorial = every combination, captures all effects
2^k runs: practical for up to ~5-6 factors
Interactions are why DOE beats OVAT
Center points detect curvature cheaply
doe-helper automates generation, recording, and analysis

## Slide 11
HANDS-ON EXERCISE
Exercise 3: Seal Strength Experiment
1. Create the seal_strength experiment from the slide
  mkdir seal_strength && create config.json as shown
2. Run: doe generate seal_strength/
3. Run: doe info seal_strength/ -- how many runs?
4. Use the simulation script: bash seal_strength/run.sh
5. Run: doe analyze seal_strength/
6. Answer these questions:
  Which factor has the largest main effect?
  Are there any significant interactions?
  Is there evidence of curvature from center points?
7. Run: doe report seal_strength/ -- open the HTML report